# 6502 CPU Emulator Design
# Hardware Emulation
## Typical hardware layout
# CPU
This is the heart of the system and controls all actions. A CPU has several critical properties which define stuff. These are:
- Address bus size in bits. This defines the physical address for memory and devices
- Data bus size in bits. This defines that maximum amount of data the cpu / devices / memory can exchange for a specific address.
- Other control information. These include interrupts, device readiness , reset of cpu or device(s) .
The CPU(6502) has basic components of:
- Register file
  - 8 bit Accumulator
  - 8 bit index X register
  - 8 bit index Y register
  - 8 bit stack pointer (fix memory block starting at 0x01FF)
  - 8 bit processor status register
  - 16 program counter
- An instruction decoder
- A system bus
  - 8 bit data bus
  - 16 bit address bus
  - 2 bits of interrupt control lines (NMI and INT)
  - 1 bit Power on reset
    - Interrupts are only handled after completing an instruction. The fetch operation before starting the next cycle checks for an interrupt. If detected – it inserts a special interrupt instruction (using an unused op code). That instruction is executed which sets the PC to the interrupt handler address and pushes the current PC and the processor status flags to the stack.
# Bus
The bus is the “spinal cord” of the system which handles all memory and device connections and routing of data. It also handles the asynchronous communications between the cpu/memory and virtual devices. Since each device must run in it own thread since they are usually doing something else while the cpu is running it own work load.
Since the 6502 only has one address bus – all devices are memory mapped devices. The bus handles mapping a device to a physical address.
# Memory
The system memory can be thought as three types:
- Memory
  - ROM
  - RAM
- Device accesses
When the CPU attempts to read/write to a memory address – the bus looks up the address and verifies the address has either ROM/RAM/Device mapped to that address (MMU). If nothing is mapped, memory returns 0x00 – which is the BRK instruction.
# Interrupt Controller (W65C22)

This Versatile Interface Adapter Java implementation is a standard memory mapped device taking 16 bytes of address space.

Figure 1: Full Specifications of the W65C22 controller
# Devices